Ducati Scrambler Sixty2 Technical specification

Engine

Type			L-Twin cylinder, Desmodromic distribution, 2 valves per cylinder, air-cooled

Displacement		399 cc

Bore x stroke		72 mm x 49 mm

Compression ratio	10,7 : 1

Power			30.2 kW (41 hp) @ 8750 rpm

Torque			34.6 Nm (3.5 kgm) @ 8,000 rpm

Fuel injection		Electronic fuel injection, throttle body diameter 50 mm

Exhaust	Exhaust system with single stainless steel muffler, aluminium tail pipe cover; catalytic converter and 2 lambda probes

Emissions		Euro 4

Transmission

Gearbox		6 speed

Ratio			1=32/13 2=30/18 3=28/21 4=26/23 5=22/22 6=24/26

Primary drive		Straight cut gears; Ratio 2.28:1

Final drive		Chain; front sprocket 15; rear sprocket 48

Clutch			Wet multiplate clutch with mechanical control

Chassis

Frame			Tubular steel Trellis frame

Front suspension	Traditional Showa 41 mm fork

Front wheel travel	150 mm (5.9 in.)

Front wheel		Lightweight alloy, 10-spoke, 3.00" x 18"

Front tyre		Pirelli MT 60 RS 110/80 R18

Rear suspension	Kayaba rear shock with fully adjustable preload

Rear wheel travel	150 mm (5.9 in.)

Rear wheel		Lightweight alloy, 10-spoke, 4.50" x 17"

Rear tyre		Pirelli MT 60 RS 160/60 R17

Front brake		320 mm disc, 2-piston floating calliper with ABS as standard

Rear brake		245 mm disc, 1-piston floating calliper with ABS as standard

DIMENSIONS AND WEIGHT

Wheelbase		1,460 mm

Rake			24°

Trail			112 mm (4.4 in.)

Total steering lock	35°

Fuel tank capacity	14 l

Dry weight		167 kg

Wet weight*		183 kg

Seat height		790 mm - 770 mm low seat available as an accessory

Max height		1,165 mm (brake oil tank)

Max width		860 mm (mirrors)

Max length		2,150 mm

Number of seats	Two-seater

Standard equipment 	Steel tank; front headlight with glass lens, LED positioning light with interchangeable surround; rear headlight with LED technology; LCD instrumentation with interchangeable surround; 18" front wheel and 17" rear wheel